## Slide 1
Reza Taghavifard
D-Charts Mesh Segmentation For fabrication
Notes: Welcome everyone to my presentation on "Quasi-Developable Mesh Segmentation for Fabrication"
This project explores techniques for converting complex 3D models into developable patches that can be fabricated from flat materials
I'll be discussing the methodology, implementation, results, and challenges encountered during this project

## Slide 2
Problem: Converting complex 3D models into quasi-developable patches
Motivation: Simplifying fabrication from sheet materials (fabric, paper)
Applications: Physical model creation, papercraft, textile design
Challenges: Minimizing distortion and number of cuts
Goal: Segment 3D meshes into regions approximating cones, cylinders, or planes
Introduction
Notes: The core problem we're addressing is how to convert complex 3D models into quasi-developable patches
Developable surfaces can be flattened onto a plane without stretching or tearing
This is crucial for fabrication from sheet materials like fabric, paper, or metal
Applications include papercraft, fashion design, architectural models, and product prototyping
The main challenge is finding a balance between minimizing distortion and reducing the number of cuts needed
Our goal is to segment 3D meshes into regions that approximate simple developable surfaces like cones, cylinders, or planes

## Slide 3
Developable surfaces: Zero Gaussian curvature everywhere
D-Charts algorithm (Julius et al., EG 2005): Basis for our approach
Existing approaches: Often result in excessive cuts or distortion
approach: Modified Lloyd iterations with conic proxies
Contribution: Balance between distortion and number of seams
Background & Related Work
Notes: Developable surfaces have zero Gaussian curvature everywhere, meaning they can be flattened without distortion
Pure developable surfaces are limited to planes, cylinders, cones, and tangent developables
Our work builds upon the D-Charts algorithm by Julius et al. from 2005, which introduced chart-based segmentation
Existing approaches often result in either excessive cuts or significant distortion when flattening
Our contribution is a modified approach using Lloyd iterations with conic proxies to better balance distortion and seam count
We've adapted these techniques to handle both smooth and polyhedral meshes

## Slide 4
The method follows a systematic approach to segment and flatten 3D meshes:
Preparing the mesh data
Initializing charts with seed points(based on Farthest Point Sampling (FPS))
Growing charts using modified Lloyd iterations
Handling special cases like high-curvature areas
Flattening the resulting patches
Method Overview
Notes: Our method follows a systematic approach to segment and flatten 3D meshes
The overall process involves:
Preparing the mesh data
Initializing charts with seed points
“I use farthest point sampling to initialize seeds. This method starts with one random face and then picks the next seed that is farthest from all existing seeds. It ensures that seeds are well distributed over the mesh, which leads to more even and meaningful chart segmentation.”
Growing charts using modified Lloyd iterations
Lloyd's algorithm comes from centroidal Voronoi tessellation – a method to evenly distribute regions around centers.
Handling special cases like high-curvature areas
Flattening the resulting patches

## Slide 5
Fitting Error: a triangle whose normal is far from the chart plane.
Compactness: triangle far away from the chart’s seed along surface.
Boundary Promotion: triangle that shares 1 edge vs 2 edges with the chart.
Cost function
Notes: To guide the chart-growing process, I use a composite cost function with three components:
Fitting Error (F) — This checks if the triangle is coplanar with the chart’s proxy. A large angular deviation from the chart normal increases the cost and discourages including highly curved triangles.
Compactness (C) — This prevents charts from becoming stretched or irregular by penalizing triangles that are far from the seed in geodesic distance. It keeps the chart spatially tight.
Boundary Promotion (P) — This encourages triangles to grow smoothly along existing boundaries, giving preference to triangles that share more edges with the chart.
Finally, these are combined using a weighted product, where I can tune the influence of each term using α, β, and γ. This multi-objective strategy helps generate well-structured, developable, and connected charts.”

## Slide 6
Results Achieved
1. Flexible Quasi-Developable Segmentation
  Successfully breaks mesh into near-developable charts
  Each chart approximates a conic surface
2. Partial Cuts in High-Curvature Areas
    Local seams (darts) help create workable 2D layouts
3. Geometry-Dependent Outcomes
  Multi-chart approach reduces cuts for some models
  Single-chart with strategic cuts works better for others
4. Polyhedral Mesh Experiment
  Algorithm identified convex polyhedron "cells"
Notes: Our implementation successfully breaks meshes into near-developable charts
Each chart approximates a conic surface, making it easier to flatten with minimal distortion
For high-curvature areas, we introduced partial cuts or "darts" that help create workable 2D layouts
An interesting finding was that the effectiveness of multi-chart versus single-chart approaches depends on the geometry
For some models, the multi-chart approach significantly reduced the number of cuts needed
For others, a single chart with strategically placed cuts worked better
In our polyhedral mesh experiment, the algorithm successfully identified convex polyhedron "cells"
This demonstrates the versatility of our approach across different types of geometry

## Slide 7
Challenges & Solutions
1. Dominant Charts Problem
  Issue: First chart expanding too rapidly
  Solution: Concurrent chart growth implementation
2. Varying Results on Total Cuts
  Issue: Multi-chart not always reducing cut length
  Finding: Outcome is geometry-dependent
3. Optimal Number of Charts
  Challenge: Determining ideal chart count
  Approach: Parameter tuning and experimentation
4. Unfolding Polyhedral Charts
  Challenge: Testing flattening on polyhedral meshes
  Status: Partially implemented, future work
Notes: One significant challenge was the "dominant charts problem" where the first chart would expand too rapidly
We solved this by implementing concurrent chart growth, ensuring more balanced chart sizes
We also found that multi-chart segmentation doesn't always reduce the total cut length
This outcome is highly geometry-dependent, which was an unexpected but important finding
Determining the optimal number of charts remains a challenge
Our approach relies on parameter tuning and experimentation to find the best configuration
Testing the flattening process on polyhedral meshes is still a work in progress
This represents an area for future development and refinement

## Slide 8
Future Work
1. Optimization for optimal chart count
  Automated determination of ideal number of charts
2. Improved flattening for polygonal models
  Better handling of sharp features and edges
3. Real-world fabrication testing Challenge: Determining ideal chart count
Notes: Several promising directions for future work include:
Developing optimization techniques for automatically determining the ideal number of charts
Improving the flattening process for polygonal models, especially those with sharp features
Incorporating anisotropic material properties into the segmentation process
Conducting real-world fabrication tests with various materials to validate our approach
These enhancements would further improve the practical applicability of our method